## Slide 1: Ash Fusion Temperature Predictions (CLSO Reconciled)
Blend Sample | DT (°C) | ST (°C) | HT (°C) | FT (°C)
100 coal | 1168.1 | 1244.5 | 1254.5 | 1351.2
5% BC | 1151.1 | 1239.3 | 1249.3 | 1292.7
10% BC | 1145.9 | 1218.3 | 1228.3 | 1303.2
15% BC | 1162.7 | 1260.1 | 1270.1 | 1331.9
100% BC | 1117.1 | 1156.9 | 1192.3 | 1252.5
Key Interpretations:
• Alkaline Fluxing Effect: Increasing the biomass proportion generally lowers the ash fusion temperatures across all stages (compare 100% coal to 100% BC). This is driven by the introduction of alkaline species (K₂O, CaO) which break down the aluminosilicate network.
• Physical Validity (CLSO): Raw predictions contained overlaps (ST > HT). The Constrained Least Squares Optimization (CLSO) algorithm successfully forced the predictions to maintain the strict thermodynamic order (DT ≤ ST ≤ HT ≤ FT).
• Non-linear Blending Behavior: The 15% BC blend shows a localized peak in fusion temperatures compared to 10% BC, highlighting that complex quaternary/quinary oxide interactions can create eutectic fluctuations before dropping drastically at pure biomass.